## Slide 1: Formulation of a Micro Demand Model for Freight Transport in Berlin
Lei Zhang

## Slide 2
Background
Objectives
Commodity Generation
Tour Distribution
Further Research
Overview

## Slide 3: Background
Cities provide attractive opportunities

## Slide 4: Background
Freight transport problems:
  Public infrastructure
  Safety
  Energy consumption
  Air pollution
  Other negative social effects
  …
Most operational models do not have sufficient behavioral detail to simulate in a representative and satisfying manner.
Freight movement involves complicated linkages among many freight agents interacting in supply chain.
Finding sufficient empirical data behind the models remains challenging.

## Slide 5: Objectives
City as a whole: help to achieve the sustainability of urban economic and freight transport growth
Private sector: maximize the utilization of all logistical resources to satisfy a city’s demand for high-qualified logistics services; reduce the total logistics cost; and ensure a sustainable goods supply for citizens
Public sector: minimize the negative effects caused by the logistical activities within urban areas to improve the city living environment
To contribute to the development of a freight demand model based on a microscopic modeling approach, which reflects the real mechanism of freight movement, describes its behavior in a quantitative way and allows for high sensitivity towards policy changes.

## Slide 6: Commodity Generation
Cities are growing more and more into pure consumption centers of goods.
The movement of vehicles is the result of the intention to move commodities, and consumption demand regulates commodity flows.
The commodity consumption of a shop is caused by individual consumers.

## Slide 7: Commodity Generation
Consumers are more willing to go to shops with high consumer appeal.
  the probability that the consumers in area z shop in shop i
  the floor area of shop i
  the distance from area z to shop i
  parametric variable
  the set of shops
  the total consumption amount of shop i for commodity k
  the probability that the consumers in area z shop in shop i
  the population in area z
  the personal consumption for commodity k
  the set of zones

## Slide 8: Commodity Generation
Average daily consumption amount of food for the shops in Berlin

## Slide 9: Tour Distribution
Trip chain data from KID (Kraftfahrzeugverkehr in Deutschland)
  2230 freight travel records in Berlin and surrounding areas
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 10: Tour Distribution
Trip chain data from KID (Kraftfahrzeugverkehr in Deutschland)
  2230 freight travel records in Berlin and surrounding areas
Chart: 
| Retial (without Food) | Food Retail | Construction & Building Material | Machines & Component | CEP Services | Unknown
 | 0.26348 | 0.11245 | 0.204 | 0.037175 | 0.15195 | 0.23095
Chart: Type of Vehicles
| ≤3.5 t | 3.5 t - 7.5 t | 7.5 t - 18 t | 18 t - 25 t
 | 0.67692 | 0.16923 | 0.092308 | 0.061538
Chart: Number of Stops per Tour
| 1 Stop | 2 Stops | 3 Stops | 4 Stops | 5 Stops | ≥6 Stops
 | 0.48 | 0.10667 | 0.10667 | 0.053333 | 0.053333 | 0.2
(Food Retail)
(Food Retail)
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 11: Tour Distribution
Distance frequency for food retail
Chart: Distance (m)
| 2000 | 4000 | 6000 | 8000 | 10000 | 12000 | 14000 | 16000 | 18000 | 20000 | 22000 | 24000 | 26000 | 28000 | 30000 | 32000 | 34000 | 36000 | 38000 | 40000 | 42000 | 44000 | 46000 | 48000 | 50000
 | 20 | 34 | 46 | 25 | 28 | 23 | 12 | 15 | 4 | 5 | 7 | 4 | 8 | 2 | 1 | 0 | 3 | 0 | 0 | 2 | 0 | 2 | 1 | 0 | 0
 | 0.082645 | 0.22314 | 0.41322 | 0.51653 | 0.63223 | 0.72727 | 0.77686 | 0.83884 | 0.85537 | 0.87603 | 0.90496 | 0.92149 | 0.95455 | 0.96281 | 0.96694 | 0.96694 | 0.97934 | 0.97934 | 0.97934 | 0.9876 | 0.9876 | 0.99587 | 1 | 1 | 1
63%
90%
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 12: Tour Distribution
Assumption and Constraints for the simple problem:
  One shop can be assigned to exactly one distribution center
  Any shop can be assigned to any distribution center
  All of the shops must assign to a distribution center
  Each distribution center has a capacity which can not be exceeded
Objective function
  Minimize the difference between observed distance distribution and modeled distance distribution
  Formal: Symmetric Kullback-Leibler-Divergence
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 13: Tour Distribution
Solution method for simple problem
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 14: Tour Distribution
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 15: Tour Distribution
Chart: Distance (m)
| 2000 | 4000 | 6000 | 8000 | 10000 | 12000 | 14000 | 16000 | 18000 | 20000 | 22000 | 24000 | 26000 | 28000 | 30000 | 32000 | 34000 | 36000 | 38000 | 40000 | 42000 | 44000 | 46000 | 48000 | 50000 | 52000 | 54000 | 56000 | 58000 | 60000 | More
Frequency | 228 | 277 | 229 | 176 | 164 | 133 | 116 | 128 | 64 | 67 | 73 | 26 | 41 | 11 | 12 | 12 | 16 | 4 | 6 | 16 | 8 | 4 | 6 | 2 | 4 | 0 | 2 | 1 | 0 | 1 | 0
Cumulative % | 0.12479 | 0.27641 | 0.40175 | 0.49808 | 0.58785 | 0.66065 | 0.72414 | 0.7942 | 0.82923 | 0.8659 | 0.90586 | 0.92009 | 0.94253 | 0.94855 | 0.95512 | 0.96169 | 0.97044 | 0.97263 | 0.97592 | 0.98467 | 0.98905 | 0.99124 | 0.99453 | 0.99562 | 0.99781 | 0.99781 | 0.99891 | 0.99945 | 0.99945 | 1 | 1
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 16: Further Research
Extension case: insert previous knowledge and observations
  Shops can be labeled according to their characteristics
    Type of goods sold
    Retail chain
  Assignment rules do not change
    Each store can still be assigned to every DC
Preference
Mandatory
DCs
DCs
Shops
Shops
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 17: Assignment Algorithm
For the most simple case: we know nothing about the reality.
For the extension case: insert previous knowledge and observations
Label | Description | Assignment Rule | Example | Priority
O | Some shops get exactly one label , and some DCs get a label from the same set O. The other shops and DCs will get a wildcard label o=wild. | Shops are assigned mandatorily to DCs with the same o Label. | Legal: (1,1), (2,2) Illegal: (1,2), (1, wild), (wild, 2) | High
H | Some shops get one label , and some DCs get a label from the same set H. The other shops and DCs will get a wildcard label h=wild. | Shops are assigned mandatorily to DCs with same h label. However, the DCs can serve shops with different H label. | Legal: (1,1), (2,2), (wild, 1) Illegal: (1,2), (1, wild) | 
P | Some shops get one label , and some DCs get a label form the same set P. The other shops and DCs will get a wildcard label p=wild. | shops are assigned preferably to DCs with same p label. However, these shops can also be assigned to any DC without their preferred label, and DCs can also serve shops with different P label. | Legal: (1, 1), (1, 2), (1, wild), (wild, 2) | Low
Label | Description | Assignment Rule | Example | Priority
O |  | Shops are assigned mandatorily to DCs with the same o Label. | Legal: (1,1), (2,2) Illegal: (1,2), (1, wild), (wild, 2) | High
H |  | Shops are assigned mandatorily to DCs with same h label. However, the DCs can serve shops with different H label. | Legal: (1,1), (2,2), (wild, 1) Illegal: (1,2), (1, wild) | 
P |  | shops are assigned preferably to DCs with same p label. However, these shops can also be assigned to any DC without their preferred label, and DCs can also serve shops with different P label. | Legal: (1, 1), (1, 2), (1, wild), (wild, 2) | Low
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 18
Label O
Retail Chain | Number of DCs | Number of shops
Aldi | 4 | 143
DM | 2 | 70
Edeka | 2 | 180
Euro Gida | 1 | 15
Getränke Hoffmann | 1 | 120
Kaisers | 1 | 133
Kaufland | 1 | 30
Lidl | 2 | 140
Metro | 1 | 7
Netto | 2 | 202
Norma | 1 | 31
Rewe | 2 | 208
Rossmann | 1 | 85
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 19
Label P
Floor area of shops (except shops from retail chains) |  | 
 |  | Floor area of DCs
 |  | > 10000
Floor area of shops (except shops from retail chains) |  | 
 |  | Floor area of DCs
Chart: 
| > 200 | 100 -200 | <100
 | 67 | 203 | 5053
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 20
Other assumptions and constraints:
  One shop can be assigned to exactly one distribution center
  All of the shops must assign to a distribution center with the corresponding label
  Each distribution center has a capacity which can not be exceeded
Objective function
  Minimize the difference between observed distance distribution and modeled distance distribution
  Formal: Symmetric Kullback-Leibler-Divergence
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 21
Assign shops to the nearest DC according to the labels
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 22
Assignment Result
  40 Distribution Centers
  6817 Shops
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 23
Assignment Result
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 24
Assignment Result
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 25
Assignment Result
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 26
Distance frequency for food retail
Notes: The probability of a distribution center being selected is a location choice selection problem with multiple alternative distribution centers. Multinomial Logit Model is used to describe the relationship between shops and distribution centers. This model could clearly express the preference information of individuals, which is a model with high adaptability. A shop is assumed to select the distribution center with the maximum utility among all the alternatives. The utility of alternatives for shop i could be described as follows:
q is an option in the selection set, that is, one of all distribution centers. 𝑉_𝑖𝑞 is the observable utility, usually expressed as
According to the utility maximization theory, any individual will choose the option with the greatest utility, Accordingly the probability that shop i chooses distribution center q is as follows:

## Slide 27: Formulation of a Micro Freight Demand Model for Berlin
Lei Zhang